## Slide 1
Environmental Noise Contamination Detection
Todd Schultz, Rahul Birmiwal, Sean Miller
Project Overview
Background
Public demand for reduced noise population forcing regulatory agencies to reduce aircraft noise limits
Certification process is expensive
Monitoring personnel used to lower risk of higher certified noise levels by noise contamination
Contamination sources include birds, insects, livestock, and road traffic
Objective
Research the feasibility of automating the detection of environmental noise contained in acoustic measurements for aircraft community noise testing.
Data
Audio Files
  72 Total
  Clean Signals
    59 Aircraft and Ambient Recordings
  Contamination Signals
    13 Animal Vocalizations
Process
Aircraft audio file split into blocks to generate features
Contamination audio file chosen and split into blocks
Contamination added to aircraft signal with desired signal-to-noise ratio
Repeated for all aircraft audio files
All generated features combined into set for model training
Results
Wide variety of feature sets and classifiers show potential to achieve an accuracy >90%
Deep neural networks under performed as compared to more traditional classifiers
Computation time of the feature set required for the combination influenced the selection of 3 combinations to optimize
3 optimized feature sets and classifiers achieve >93% cross-validation accuracy
Performance of all 3 degraded when tested against randomized scenarios
Increased fidelity of DWT5 did not out perform DWT4
Challenges
How To Turn Audio Into Features
We separated each audio file up into blocks of an equivalent length and then processed the features for each block. Blocks from which features were generated could contain overlapping audio.
How To Quantify Contamination Levels
The audio recordings that were used only had a single source of noise allowing us to combine aircraft or ambient signals with contamination to create a larger data set than the 66 files. This also allowed us to control the signal-to-noise ratio.
Limitations
Due to the small size of potential contamination audio, the models are not as accurate when classifying new sources of contamination.
One recommendation that we do have at this time is that we suggest that more data is provided to fully enumerate the possible contamination classes that would exist near the test site.
Methods
Our investigation into the viability of automated detection of environmental noise contamination is broken into two parts. A broad assessment of feature sets and models followed by a deeper investigation into three of the best performing pairs.
Broad Investigation
Objective: To gain insight to which broad categories of feature sets and model combinations might provide the best prediction accuracy
Signal-to-noise ratio held at 6 dB
Block size limited to only 1 seconds or 2 seconds
Used default hyperparameters and settings when training models
Deep Investigation
Objective: To optimize a limited set of feature set and model combinations for their best performance and subject them to rigorous testing to understand real-world performance
  Optimize the models hyperparameters.
  Randomize the signal-to-noise ratio.
  Randomize the percent of a block that contains contaminated audio.
  Randomize which blocks are contaminated.
  Vary all of above parameters through Monte-Carlo simulation.
Broad Investigation Results
Deep Investigation Results
Acknowledgements
We would like to thank our sponsor for the project, Steven Underbrink as well as our Data Science Capstone advisor: Dr. Megan Hazen, University of Washington.
The three feature set, classifier pairs selected for detailed study are as follows:
 | F1 score | Accuracy | FNR | FPR
DWT5 | 93.4% | 93.6% | 10.4% | 2.4%
DWT4 | 93.6% | 93.8% | 10.1% | 2.2%
CEP26 | 93.6% | 93.9% | 10.3% | 1.9%
Performance summary of optimized feature set and classifier pairs for detailed study subjected to randomized signal blocks contaminated
Model: Bagged Trees
Feature: Wavelets (Coiflet2, 5 level, T=2s)
Best overall with accuracy of 94.2%
Model: Bagged Trees
Feature: Wavelets (Coiflet2, 4 level, T=2s)
Accuracy of 93.3%
Model: Cubic SVM
Feature: Cepstral (26 feature T=2s)
Best non-NN, non-wavelet performer with accuracy of 92.8%
Signal-To-Noise Ratio – Parameter Sweeps
Recommendations
Continue with the DWT4 and CEP26 feature sets and classifiers
Expand the data sets with additional data, more constructed scenarios, and with variation in the signal-to-noise ratio
Development method to compute the effective signal-to-noise ratio for the scenario with a reduction in the proportion of the signal block contaminated
For each of the optimized feature set and classifier pairs, we observed that as the signal-to-noise ratio increased, this resulted in less accuracy due to the models inability to detect contaminated blocks.
Glossary / Reference
Mel Scale
A scale of pitches that is based on human perception to judge the non-linear distance between pitches.
Mel-Frequency Cepstral Coefficients (MFCC)
Coefficients that are derived from a non-linear transform of a spectrum that are equally spaced on the mel scale.
Signal-To-Noise Ratio
A ratio comparing the level of a clean signal to the level of the background noise.
Wavelet Transform
A representation of a square-integrable signal using an orthonormal basis formed by scaled and shifted versions of a chosen "mother wavelet." The Wavelet Transform is advantageous over the Fourier Transform in representing finite, non-stationary and/or non-periodic signals.
Coiflet2
Class of "mother wavelet" with 2 vanishing moments. A type of discrete wavelet invented by renowned mathematician Ingrid Daubechies with the special property that both its low-pass and high-pass filter constituents have vanishing moments.