## Slide 1: Data Pipeline for Environmental Noise Contamination Detector
Todd Schultz, Sean Miller, Rahul Birmiwal
28 Nov 2018

## Slide 2: Outline
Problem statement
Available data
Issues
Preliminary insight
Feature set options
Conclusions

## Slide 3: Problem statement
Aircraft certification requires flyover noise measurement
Environmental noise contamination is costly
  Adds time to repeat required conditions
  Potential to fail certification
Source include
  Bird chirps
  Wildlife/livestock vocalizations
  Traffic noise
Use 3 engineers for monitoring
Kevin Cole from Pacific Coast, USA CC-BY 2.0

## Slide 4: Proposal
Create an automated environmental contamination detector based on acoustic signals
Feasibility study
  What’s the potential?
  Roughly best feature set
  Roughly best algorithm

## Slide 5: Available data
Time series audio recordings near major international airport
Represents 3 days of measurement
  One day each in November 2017, December 2017, and January 2018
  49 aircraft recordings
  7 wildlife noise
  10 ambient
Microphone installation

## Slide 6: Available data
Professional recorded and labeled wave files
Wind screen used to reduce wind noise
No missing time series data points
Recorded at 51.2k samples/second
Usable bandwidth from 4.6 Hz to 20 kHz
Scientific instrumentation grade equipment
Pressure amplitudes have been normalized for public release
  Feature selection will normalize again to remove overall signal energy
  Done to remove sound level variation due to propagation distance

## Slide 7: Available data
Bird chirp (bird01.wav)
Jet aircraft (plane8.wav)

## Slide 8: Issues
Propagation distance effects on amplitude
  Normalize time-series levels
  Normalize features to remove signal power
Imbalance between classes
More clean aircraft signatures than contaminated
Public domain recordings for wildlife vocalizations exist
Superposition to create new, contaminated signal
  Can use to test performance versus signal-to-noise ratio
Data management
  Each signal will produce 50-100 blocks of features
  Each block of features maybe 10-1,000’s of features

## Slide 9: Preliminary insights-octave spectrum
Bird chirp (bird01.wav)
Jet aircraft (plane8.wav)

## Slide 10: Preliminary insight
Octave spectrum
  10 bands = 10 features per octave spectrum
  31.5, 63, 125, 250, 500, 1000, 2000, 4000, 8000, 16000 Hz bands
  Spectrum shape visibly different for bird and aircraft
  Spectrum shape of aircraft changes as function of position relative to microphone
Thoughts
  May need to extract representative blocks and remove ‘quiet’ blocks
  Need to ensure sample blocks of the directivity of aircraft noise

## Slide 11: Feature set options
Numerous options available for feature generation
(1/n) Octave band spectrum
Cepstrum
Short-time Fourier Transform
Wavelets
?

## Slide 12: Conclusions
Time series data is ready
Data management could be cumbersome
Time series signals may require pre-processing
Many feature generation options available
Project goal supports testing a vary of feature choices